## Slide 1: Systems / Real-time / ProcessorExpert
Roman Stutz and Florian Bucher
INTRO FS15

## Slide 2: Agenda
System types
Real-time
  Hard / Soft
ProcessorExpert
Lab – Questions

## Slide 3: Systemtypes
Interactive Systems
Reactive Systems
Transforming Systems
Notes: Transforming Systems
- e.g. Parser
Data processing quality (no latency, no data loss)
Huge Throughput
Optimization for system load and memory usage
Reactive Systems
e.g. Thermostat: Measures temperature and reacts with powering up the fan if the cpu is going to overheat
Control loop for external event
Guaranteed response time
Real-time
Interactive System
e.g. common calculator: Takes input, applies some magic and returns an output
Short response time
High system load
HMI (Human Maschine Interface)

## Slide 4: Real-time
React to real word ....
.... With the correct result
.... At the correct time
.... Independent of system load
.... In a deterministic and foreseeable way
Example:
Platform announcements at the train station as soon as you exit the train.

## Slide 5: Hard- / Soft real-time
Hard
  Reaction always at the same time
  No deviation allowed
Soft
  Reaction within time span
  Little deviation allowed

## Slide 6: ProcessorExpert
Code generator for hardware component drivers
Each component consists of three parts
  Methods
  Events
  Properties
Notes: Methods
-Procedures that can be executed
-Function calls
Events
-Indication of state changing
-Usually implementation of ISRs
Properties
-Modify/Customize object behavior
-Set during design-time

## Slide 7: ProcessorExpert: Flow

## Slide 8: LabQuestions

## Slide 9: What is the advantage of using *.PEupd compared to use the files in the repository? What are advantages and disadvantages of using the Git repository files?
LabQuestion #1
Depends on context:
If components are used in multiple projects, a git repo will share fix/adjustments to all other projects.
But it is easer and more user-friendly to import just a file into the ProcessorExpert then specifying and configure the git repo.

## Slide 10: You could use either BitIO or the LED component: What are the pros and cons of each approach?
LabQuestion #2
LED is wrapper for BitIO
Better abstraction for LED component(+)
Additional access to pwm and anode/cathode
Code overhead (-)
Notes: BitIO: just named signal

## Slide 11: What are the advantages of using a tool like Processor Expert? What could be the disadvantages?
LabQuestion #3
Less code writing
Focus on more important problems
General code, not always optimized

## Slide 12: What would be a typical method for an character display component? What would be a typical property or event?
LabQuestion #4
Method: WriteLine()
Event: OnError
Notes: WriteLine(): Writes a line of characters to the display
OnError: If display could not be accessed for writing.

## Slide 13: From the GitHub you could download the repository as zip file and then unpack it at the right location. What is the advantage of cloning it instead?
LabQuestion #5
If there is a change in the repo, with the zip method, you have to redownload the repo and copy / replace / merge the file by hand. With the cloned repo git will do most of the work for you.
Notes: See LabQuestion #1